## Slide 1: Computer Aided Engineering
Introduction to EES (Engineering Equation Solver) Lecture 2
The unit system,
Built-in functions

## Slide 2: Contents
EES introduction tutorial (4 Lectures)
  Solving nonlinear & implicit equations (Lect 1)
  Formatting of equations (Lect 1)
  The unit system (Lect 2)
  Built-in functions (Lect 2)
  The Options menu (Lect 3)
  Parametric studies & plot basics (Lect 3)
  Lookup tables (Lect 4)
  Plots (Lect 4)
0:35

## Slide 3: The Unit System
EES is fully unit-aware
The Unit System is the first thing that should be set at the start of a project
  Set from the Options menu
  Safer to explicitly set units using directives (which will override dialog settings):
    $UnitSystem SI MASS DEG KPA C KJ
Create a new EES worksheet and save it as
  EES Lecture 2.1 – UnitSystem.ees
  Add the $TabStops and $UnitSystem directives
0:40

## Slide 4: The Unit System
Individual constants can be assigned units:
    m = 25 [kg]
    a = 2.5 [m/s^2]
    F = m * a
Units cannot be assigned for equations, but EES will automatically determine the units for F (shown in purple in the results window)
0:45

## Slide 5: The Unit System
Hint: Check the “Check units automatically” and the “Set units automatically when possible” checkboxes in the Options menu > Preferences > Options tab, then press Store and select the EES.PRF file to make this permanent. You may also want to select the other options as indicated.
0:45

## Slide 6: The Unit System
0:45

## Slide 7: The Unit System
Variables are mapped in the
Options > Variable Info menu
  The units shown for F are [kg-m/s^2]
  Change this to [N] for F and observe that EES gives no warnings
  Now change the units for F to [kN] and check out the warning!
  Change the unit for m to [lbm] and set the unit for F as [N] and check out the warning!
0:50

## Slide 8: The Unit System
0:45
Guess values
Lower and Upper limits
Display
Units
Automatically assigned units in purple

## Slide 9: The Unit System
0:45
No unit problems with F in [N]
Unit problems with F in [kN]

## Slide 10: The Unit System
EES also allows unit conversions
  Suppose we have the equation F = m a, but we want F in kN. If we set [kN] for F in the units map, we will get a warning
  So we do this:
  F = m * a * convert(N, kN)
  "Alternatively you can do this, but then you need to know the conversion constant"
  F_1 = (m * a) / 1000 [N/kN]
  F_2 = m * a * 0.001 [kN/N]
0:55

## Slide 11: The Unit System
  We can even convert between Imperial and SI units:
  m_3 = 10 [lbm]
  a_3 = 3.5 [m/s^2]
  {F_3 = m_3 * a_3} "This would give an error"
  F_3 = (m_3 * convert(lbm, kg)) * a_3
0:55

## Slide 12: The Unit System
  We can also assign units to constants in situ to make a constant clearer, for example:
  "This is clearer than the next..."
  time = 3.5 [h] * 3600 [s/h]
  "The fact that this is 3.5 hours is not as apparent!"
  time = 12600 [s]
EES online examples:
  Examples/Units conversion/Checking units and unit conversion (HeatEx.EES)
  Examples/Getting Started with EES/Converting units function (Convert.EES).
0:00

## Slide 13: Built-in Functions
EES provides built-in functions in the following categories:
  Mathematics
  Fluid properties
  Solid / Liquid properties
  EES Library routines
  External routines
Example code can be pasted
Function Info (Help)
Create a new EES worksheet and save it as
  EES Lecture 2.2 – BuildInFunction.ees
0:05

## Slide 14: Built-in Functions
A Maths example
  x=cos(Value) "This is exactly as it was pasted"
  Now it is up to you to modify the statement as you want it. Maybe you wanted to do the following:
  theta = 30 [deg]
  x_coordinate = cos(theta)
  Or
  z = cos(33) "Hardcoding values is rarely a good idea"
0:10

## Slide 15: Built-in Functions
Maths examples
  LogValue = log10(100) "The log10(Value) was pasted!"
  Use of trailing _ to prevent confusion
  gamma = gamma_(Value) "Note the trailing underscore“
  "Young’s Modulus – note underscore"
  T = 140 [C]
  E = E_(Aluminum, T) "Note American spelling!"
  Integral equations
  EES can perform numerical integration and differentiation. How would you solve the following?
  "An integral equation – be sure to switch off complex numbers"
  y = Integral(x^3, x, 0, 3, 0.06)
0:10

## Slide 16: Built-in Functions
Property examples
  For properties one typically has to specify conditions such as pressures and temperatures. Furthermore, one has to specify the material (a solid or a fluid).
  The simplest example is probably the density of a gas. Let’s paste the density for air from the Fluid Properties Function Info dialog:
  rho_1=Density(Air,T=T_1,P=P_1)
0:10

## Slide 17: Built-in Functions
  rho_1=Density(Air,T=T_1,P=P_1)
Note the following:
  A name for the variable is automatically given, which you may want to change
  The first argument is the fluid name. This name is actually a string and should strictly speaking have single quotes around it. However, as long as names don’t contain spaces, this will work.
  The conditions for pressure and temperature are given next. The user should either hardcode these, or provide values for T_1 and P_1.
0:10

## Slide 18: Built-in Functions
Fluid property example
  "T and P are hardcoded, but what are their units?"
  rho_1 = Density(Air, T=25, P=100)
  "It is actually better to do this (the units are now clear also):"
  T1 = 25 [C]
  P1 = 100 [kPa]
  rho_2 = Density(Air, T=T1, P=P1) "T1, P1 are variables!"
  h = Enthalpy(Water, T=T1, P=P1)
  v_specific = Volume(Water, T=T1, P=P1)
0:10

## Slide 19: Built-in Functions
Solid property example
  "Young’s Modulus – note the underscore"
  T = 140 [C]
  E = E_(Aluminum, T) "Note American spelling!"
0:10

## Slide 20: Built-in Functions
A short note on formatting
  Readability of typed equations is extremely important, however many people are just too lazy to think of the advantages. The original pasted code was:
  rho_1=Density(Air,T=T_1,P=P_1)
  Is it not much easier to read when the code looks as follows?
  rho_1 = Density(Air, T=T_1, P=P_1)
  Use spaces liberally around the equals sign, operators as well as after separators (the comma) to highlight separate sections.
  It becomes much more important when you have complex equations with many terms and brackets.
0:10

## Slide 21: Tips
Shortcuts
  Right-click on a variable in the equations window to set unit & display formatting
  Right-click on a message to jump to the equation
  Learn to use the toolbar
  Be sure to check out:
    Examples>Integration>Double Integration.
0:25

## Slide 22
End of Lecture 2
0:05