## Slide 1: Computer Aided Engineering
Introduction to EES (Engineering Equation Solver) Lecture 4
Lookup tables,
Plots & Graphs

## Slide 2: Contents
EES introduction tutorial (4 Lecures)
  Solving nonlinear & implicit equations (Lect 1)
  Formatting of equations (Lect 1)
  The unit system (Lect 2)
  Built-in functions (Lect 2)
  The Options menu (Lect 3)
  Parametric studies & plot basics (Lect 3)
  Lookup tables (Lect 4)
  Plots (Lect 4)
0:35

## Slide 3: Lookup Tables
Lookup Tables and Lookup Files (residing on the disk) provide a means of using tabular information in the solution of equations
A good example is the variation of a property such as air density with temperature
Conveniently (again!), EES uses a spreadsheet approach.
(EES Lecture 4.1 - SimpleLookupTable.EES):
0:08

## Slide 4: Lookup Tables
This is how the air density changes with temperature at ambient pressure. One could, of course, fit a mathematical function through that, however it is much simpler and more flexible to put the data in a lookup table or lookup file:
0:10

## Slide 5: Lookup Tables
Lookup data can be accessed using two functions:
Using the Lookup function, one specifies a specific row and column and retrieve a value for the other column for the same specified row
The Interpolate function is much more useful. In essence it works like the Lookup function, except that the retrieved value could fall between table rows. EES would then interpolate for this value, using several interpolation schemes
There are 2 ways to specify Lookup table data:
Create and use a lookup table in EES and add the required data to it (shown on the previous slide). It can be directly pasted from Excel with headings and units for example (using Paste Special)
Add the data to a text file and simply tell EES about the file. The file has the following format:
0:15

## Slide 6: Lookup Tables
0:15
Number of rows
Number of columns
Minus sign indicates that heading data is present
Number format (Auto 3-digit)
Column title
Column unit
First column (T)
Second column (rho_air)
One could also omit the file headings and just specify the column data, but that is far less flexible and user-friendly!
Heading
data

## Slide 7: Lookup Table Creation
A lookup table is created from the Table menu:
Data and headings can be manually entered or pasted from a text file or Excel:
0:15

## Slide 8: Lookup Table Usage
"Format:
TableName, RowNo (or RowName), ColNo (or ColName)"
T_1 = Lookup('Lookup 1', 4, 1) "The table name is a string"
rho_1 = Lookup('Lookup 1', 4, 2)
0:25

## Slide 9: Lookup Table Usage
"Instead of a column number, we could specify the column by name via a string..."
T_2 = Lookup('Lookup 1', 5, 'T') "T is a string!"
rho_2 = Lookup('Lookup 1', 5, 'rho_air')
"This way, row is a variable, which is much more flexible"
row = 6
T_3 = Lookup('Lookup 1', row, 'T')
rho_3 = Lookup('Lookup 1', row, 'rho_air')
0:25

## Slide 10: Lookup Table Usage
"More useful interpolate commands"
"Format: TableName, Col1Name, Col2Name, ColValue"
"Note the single quotes!"
rho_4a = Interpolate('Lookup 1', 'T', 'rho_air', 'T'=65)
"As long as strings have no spaces, we can omit the quotes"
rho_4b = Interpolate(Lookup1, T, rho_air, T=65)
"We could also provide the value for the density column and retrieve the temperature"
T_4 = Interpolate(Lookup1, T, rho_air, rho_air=1.2)
0:25

## Slide 11: Lookup Table Usage
"It is mostly a good idea to specify the properties such as temperature as variables"
T_5 = 65 [C]
rho_5a = Interpolate(Lookup1, T, rho_air, T=T_5)
"The lookup table can also reside in a disk file. Better to use string format for file name as file names often have spaces"
rho_5b = Interpolate('Lookup 1.txt', T, rho_air, T=T_5)
0:25

## Slide 12: Lookup Table Notes
A table can be saved to disk (or opened) from the Table menu as shown.
The saved file format can be text (txt), binary (lkt) or comma seperated variable (csv).
EES’s built-in libraries are binary and are stored in the Userlib directory as shown.
0:25

## Slide 13: Lookup Table Notes
Note: There are 5 versions of the Interpolate function:
INTERPOLATE uses cubic interpolation
INTERPOLATE1 uses linear interpolation
INTERPOLATE2 uses quadratic interpolation
INTERPOLATE2D does a 2-D interpolation,
stored in a table.
INTERPOLATE2M does a 2-D interpolation,
stored in a matrix
0:25

## Slide 14: Lookup Table Notes
As shown before, one can omit the string quotes in the Interpolate function, and in many (most) other built-in EES functions, provided there are no spaces in the strings.
However, this does not work for the Lookup function. In the Lookup function, the table or file name can omit the quotes, but the column names cannot! This is so since columns can also be numbered.
0:25

## Slide 15: Advanced Lookup Table
A more extensive example is the International Standard Atmosphere (ISA) which gives the properties of the atmosphere at different altitudes
In the example, four properties are listed against each other. One can interrogate any two columns at a time.
Please refer to “ISA Atmosphere.xls”
(EES Lecture 4.2 – ISA LookupTable.EES)
0:08

## Slide 16: Advanced Lookup Table
This is what the International Standard Atmosphere temperature with height looks like. It is obviously not going to be easy to fit a mathematical function through that!
0:10
Note: Use LINEAR interpolation here and NOT CUBIC

## Slide 17: Advanced Lookup Table
The Lookup table would look as follows:
0:15

## Slide 18: Advanced Lookup Table
"Obtain the temperature and the density at a height of 4800m"
T_1 = Interpolate('ISA', 'Height', 'Temperature', 'Height'=4800)
rho_1 = Interpolate('ISA', 'Height', 'Density', 'Height'=4800)
"At what height would the pressure be 80 kPa?"
H_1 = Interpolate('ISA', 'Height', 'Pressure', 'Pressure'=80)
0:25

## Slide 19: Plots & Graphs
Plot basics have been introduced in lecture 3. In this section we will introduce some of the more advanced features of plots and graphs:
What is a plot and a graph?
How EES plots graphs from data
Multiple graphs on a plot
Axes, scales, line types, marker symbols, grid lines
Editing plot data
Annotating a plot, text data, editing titles
0:08

## Slide 20: Plots & Graphs
In EES plots (like parametric tables and lookup tables) are all housed in a dedicated window that is accessible through the Windows menu or the toolbar.
0:08
All plots are housed in the one plot window
Each plot occupies a new tab

## Slide 21: Plots & Graphs
A graph is a line on an X-Y axis. A plot may consist of a number of graphs on the same X-Y axis.
0:08

## Slide 22: Plots & Graphs
There are 3 types of graphs that can be plotted with EES:
X-Y plots
Bar plots
X-Y-Z plots (3-dimensional)
  Surface plots
  Contour plots
0:08

## Slide 23: Plots & Graphs
How EES plots graphs from data:
EES plots graphs from any type of “array”. Parametric tables, lookup tables and ordinary arrays (matrices) all qualify as sources for graphs.
EES iterates through the arrays and plots y[1] vs x[1], y[2] vs x[2], y[3] vs x[3] etc
The source is the first selection that should be made when creating a graph.
The source selection will automatically load the relevant variables in the X-axis and Y-axis variable list boxes.
0:08

## Slide 24: Plots & Graphs
We demonstrate this by creating data and storing it in the different “array” types (Lecture 4.3 - Plots and Graphs.EES):
We create two parametric tables as functions of sine and cosine
We also create data and store it in an array
Lastly, we place some data in a Lookup Table
0:08

## Slide 25: Plots & Graphs
Now let’s plot graphs from these “arrays”
The first step after choosing “X-Y Plot ” from the menu is to select the data source, the three alternatives being shown here:
0:08
Note the data source options
Note the variables automatically being loaded for the selected data source

## Slide 26: Plots & Graphs
More on data source selection:
Since we have created two parametric tables, we have to select the instance we want to plot from:
0:08
Note the table source options
Note the variables automatically being loaded for the selected data source

## Slide 27: Plots & Graphs
Let’s now put all these graphs on a single plot
Plot the first graph from the parametric table Table 1 (the sine function) as shown before, choosing the variables x for the X-axis and y for the Y-axis:
Normally one wants to plot all the data in the table or array, but one can actually specify the start and end indices
Check the “Spline fit”, “Auto Update” and “Add legend item” checkboxes and choose a symbol and a colour and press OK.
0:08
The “Automatic Update” checkbox will ensure that the graph is automatically updated when the data in the table or array changes. This is mostly desired, but when the same parametric table is used to generate different curves, one may not want to check this option.

## Slide 28: Plots & Graphs
To plot subsequent graphs on the same plot, choose “Overlay Plot”
The same plot setup dialog appears. We must now choose the second parametric table as source
Check the “Spline fit”, “Auto Update” and “Add legend item” checkboxes
Note that EES automatically chooses the next symbol and colour
Press OK.
0:08
Note the legend

## Slide 29: Plots & Graphs
We can also plot the data from the array table (and the lookup table) in the same way
Note that there is only one array table, whereas it is possible to create several parametric and lookup tables
Like with tables, one can plot any range of the data
Arrays can also show the array index at each point
Note that EES automatically chooses the next symbol and colour
Press OK
Note that the new graph exceeds the Y-axis limits
0:08
Graph from array
exceeding Y-limits

## Slide 30: Plots & Graphs
We can fix the scaling (range) of any axis by simply clicking on the axis, which would bring up the following dialog:
We could select “Automatic scaling” or one could manually enter appropriate limits
We could also change to log scaling, switch grid lines on, change the font, font colour and text angle and even the number format from this dialog
Note the array indices on the ya[i] – curve.
0:08

## Slide 31: Plots & Graphs
We can also edit graphs after creation. Simply right-click in the plot area to produce the “Modify Plot” dialog:
We can
  Remove a graph
  Change line and marker types
  Show every n’th marker
  Choose the smoothing
  Set Auto updating
  We can connect the graph to a different data source through the Data button
  Choose the Y-axis and error bars
  Set border and grid attributes
  Swap the X and Y axes
0:08

## Slide 32: Plots & Graphs
It is easy to edit plot titles and add text and other graphics to a plot. To do this, activate the Plot Toolbar via the Plot menu or by right-clicking or double-clicking in the empty margin outside of the plot area:
The Graph value cross-hairs can be invokes by keeping the Ctrl+Shift keys down and moving the mouse pointer over the graph area. The X-Y values are displayed at the bottom of the graph
0:08
Add text tool
Add graphics tools
Graphics orientation tools
Graph value cross-hairs
Graph zoom tool
Cross hairs and X-Y values

## Slide 33: Plots & Other Outputs
Plots (like tables and formatted equations) can be copied from EES and pasted in other applications such as MS Word.
The Professional version of EES also has a MathType interface for seamless exchange between EES and other applications
The Professional version of EES also has a convenient built-in Report Writer which students can use to report on the findings of their EES study
Lastly, one can also export the report in PDF format.
0:08

## Slide 34
The End of Lecture 4
and the Introductory EES Course
0:05