## Slide 1: Computer Aided Engineering
Advanced EES (Engineering Equation Solver) Lecture 5
Min/Max,
Uncertainty Analysis

## Slide 2: Contents
EES advanced tutorial (2 Lectures)
  Min/Max analysis (Lect 5)
  Uncertainty analysis (Lect 5)
  Input and output (Lect 6)
  Advanced features (Lect 6)

## Slide 3: Min/Max
Min/Max is used to find the minimum or maximum of an undetermined variable in an equation set for which there is at least one degree of freedom.
These equations have no degrees of freedom:
This is because y can only have one value as x and z have been specified. Hence there are no independent variables in this set of equations that EES can vary.

## Slide 4: Min/Max
We can give the previous set of equations one degree of freedom by removing one of the specified (fixed) constants:
Since x is no longer fixed, the solution y has one degree of freedom – it depends on what x or z is. If the second equation was removed too, y will have two degrees of freedom.

## Slide 5: Min/Max
The following also has no degrees of freedom:
The set of two equations forms the solution (intersection) of the two curves. By removing the second equation, the first equation will have one degree of freedom – y depends on x, with x undefined. We can now use EES to vary x to find the maximum point of y:

## Slide 6: Min/Max
We can use EES to find the maximum of the black curve if EES is allowed to vary x – i.e. one degree of freedom.

## Slide 7: Min/Max
Lets create a simple Min/Max search using the projectile movement example we used earlier in lecture 3, saving a copy of it as:
  (Lecture 5.1 - SimpleMinMax.EES).

## Slide 8: Min/Max
  Find the angle that will maximise the distance s the projectile will travel for u = 30 m/s through a parametric table
  Find the same angle just using the Min/Max functionality (u = 30 m/s)
  Find the required angle that will hit a target at 60m (u = 30 m/s)
  Find the required velocities for a range of angles that will yield a range of exactly 60m!

## Slide 9: Min/Max
Remember, the basic equations of motion were:
  "The velocity components"
  u_x = u * cos(theta)
  u_y = u * sin(theta)
  "Time needed to max distance"
  t = 2 * u_y / g#
  s = u_x * t
0:10

## Slide 10: Min/Max
1. Running the parametric table with varying theta shows the optimal angle to be 45 degrees and the distance s to be 91.77. Note however, that with differently selected increments of theta that did not include 45 deg (40, 50 and 60 deg for example), we would not have arrived at 45 degrees!

## Slide 11: Min/Max
2. Using Min/Max:
The Min/Max functionality is selected from the Calculate menu:
Using the Min/Max functionality, EES will first check the syntax of the equations in the Equations window. If no errors are found, a dialog window will appear presenting the variables in two lists.
There must be at least one degree of freedom – i.e. a variable that have not been assigned a fixed value so EES can vary it.

## Slide 12: Min/Max
Click the Maximize button above the left list (in this case).
The variable which is to be minimized/maximized
The independent variable(s) whose value(s) will be changed by EES in searching for the minimum / maximum
One needs to set realistic bounds for the independent variable(s).
It is necessary to select as many independent variables as there are degrees of freedom in the Equations window. The number of independent variables which must be selected is indicated above in the right-hand list.

## Slide 13: Min/Max
3. Find the required angle that will hit a target at 60m (u = 30 m/s):
  "To be able to determine the required angle to hit a precise 60m target for an initial velocity u = 30 [m/s], we define a variable deltas to force the calculation of the angle using the Min/Max Table functionality. Remember that we cannot specify theta = 45 [deg] now as EES will vary it to try to minimise deltas and force s = 60 [m]."
  s_max = 60 [m]
  "When deltas = 0, s = 60 m"
  deltas = abs(s - s_max)
0:10

## Slide 14: Min/Max
We then minimize deltas (EES will vary theta), forcing s to be 60 m:
We find theta = 20.42 deg

## Slide 15: Min/Max - Table
4. Find the required velocities for a range of given angles that will each yield a range of exactly 60m. Here we let EES search for u , so we cannot specify u, but we specify theta in the parametric table.
With the Min/Max Table you can search for a series of solutions in a parametric table
Each run of the table will yield a specific Min/Max solution!

## Slide 16: Min/Max - Table
We now need to perform the Min/Max analysis on the table:
  Ensure that in the parametric table theta varies between 0º and 90º
  As before we define s_max = 60 [m] as the distance we want to achieve
  As before we minimise for deltas to force s to be 60 [m]
  This time however, EES will find the values of u for us, so we cannot specify u.
  Hint: To be able to minimise for deltas, deltas has to be in the parametric table!

## Slide 17: Min/Max - Table
The plot shows the velocity that was calculated for each angle given in the table to hit the 60m target.

## Slide 18: Min/Max
Lets look at another case where we would use the minimize functionality:
How would we fit a least squares polynomial through the data?
Lecture 5.2 Linear Regression.EES
The data

## Slide 19: Min/Max
To do this problem efficiently, we will utilise the Duplicate statement:
Instead of writing:
  y[1] = sin(0); y[2] = sin(15); … y[10] = sin(135); etc…
One could write:
  N = 10
  Duplicate i = 1, N
  theta[i] = (i-1) * 15
    Y[i] = sin(theta[i])
  End
This actually expands the two lines in the “loop” 10 times, with i being 1, 2, … 10, so this is NOT a loop! The same equation is NOT actually being used!

## Slide 20: Min/Max
N = 10
DUPLICATE i = 1,N
X[i] = Lookup('Lookup 1', i, 'X')
Y[i] = Lookup('Lookup 1', i, 'Y')
YP[i] = a_0 + a_1 * X[i] + a_2 * X[i]^2
END
sigma = sum((YP[i] - Y[i])^2, i = 1, N) “RMS”
Lecture 5.2 Linear Regression.EES

## Slide 21: Min/Max
Lecture 5.2 - Linear regression.EES
We minimize sigma by varying a_0, a_1 and a_2 simultaneously.
How many possible combinations of a_0/1/2 could there be? EES does it all for us! Automagically!!!

## Slide 22: Uncertainty Analysis
Uncertainty Propagation determines the uncertainty of up to 12 calculated variables as a function of the uncertainties of one or more measured values upon which it depends.
In many experiments, an important quantity is not directly measured but is rather calculated as a function of one or more variables that are directly measured, i.e., Y = f( X1, X2, ....).
The measured variables, X1, X2, etc. have a random variability which is referred to as its uncertainty. In EES, that uncertainty is displayed with a ± symbol, e.g., X1 = 300 ± 2.

## Slide 23: Uncertainty Analysis
As an example, let’s once again consider the projectile model (Lecture 5.3 - SimpleUncertainyAnalysis.EES).
Lets assume there is an uncertainty of 1.5 m/s in the initial velocity u, and an uncertainty of 3 degrees in the angle theta.
What would be the variation in the distance s that we could expect?

## Slide 24: Uncertainty Analysis-Table
However, we could also do an uncertainty analysis on a parametric table and vary parameters AND still do an uncertainty analysis on each run!

## Slide 25
End of Lecture 5
0:05