## Slide 1: Computer Aided Engineering
Introduction to EES (Engineering Equation Solver) Lecture 1
Solving and formatting
equations

## Slide 2: Contents
What is EES?
Features of EES
EES introduction tutorial (4 Lectures)
  Solving nonlinear & implicit equations (Lect 1)
  Formatting of equations (Lect 1)
  The unit system (Lect 2)
  Built-in functions (Lect 2)
  The Options menu (Lect 3)
  Parametric studies & plot basics (Lect 3)
  Lookup tables (Lect 4)
  Plots (Lect 4)
0:35

## Slide 3: What is EES?
EES (pronounced “Ease”) is a general purpose equation solver, modeling and analysis tool which has started life specifically for the purpose of engineering education
It is quite capable (it is also used in industry) and is more than adequate for engineering education purposes
Its main claim to fame is that past students have used it with “ease”
  Students find it far easier to use than any other software they have been introduced to, including:
    Mathematica
    Matlab
    Mathcad
0:37

## Slide 4: Advantages of EES
It requires no real programming (although you can!)
Implicit (iterative solver) – equations in any order
It is geared towards engineering problems
Units enabled and unit conversion routines
Formatted equations view with Greek letters and maths symbols
Lots of online example programs
Excellent online help and online manual
It comes FREE to the entire Faculty – BOTH students and staff!
Students can take it home – it is small in size!
We will use it extensively throughout your entire Engineering course, so spend the time and learn it thoroughly now!.
0:38

## Slide 5: Features of EES
Excellent engineering features:
  Lookup tables with linear-, cubic- and quadratic interpolation
  Regressions
  Plots and overlay plots
  Diagram window (User Interface)
  Animation (Cool!)
  Built-in property library - thermo, fluid and material properties (easily extendible by users)
  Predefined engineering constants
Excellent engineering analysis features:
  Parametric studies
  Uncertainty propagation
  Min/Max.
0:39

## Slide 6: Features of EES
Maths capabilities include:
  Numerical integration and differentiation
  Complex numbers and angles
  Bessel functions
  ERF and ERFC (Gaussian Error Functions)
  Gamma function
  Real and imaginary numbers
  Interpolation (2-D and 3-D)
  Numerous external libraries.
0:40

## Slide 7: The EES Help System
EES’s Help system comprises of a standard Windows help system as well as a complete user’s manual in PDF format. You will find both extremely helpful and easy to use
Students are strongly encouraged to study the first two chapters of the PDF EES manual. A small time investment now to do this will save you many hours of struggling to figure out how things work at a later stage.
This cannot be emphasised strongly enough!!!
There are a large number of examples on just about every topic included with EES – just check out the Examples menu
0:40

## Slide 8: EES Tutorial 1
In this tutorial:
Solving nonlinear and implicit equations
Formatting an equation
0:40

## Slide 9: Solving nonlinear Equations
How would you solve the following?
And an implicit equation in f such as the following?
0:41
Probably by substitution !
Iteratively !

## Slide 10: Solving Equations
Create a new EES worksheet and save it as
  EES Lecture 1.1 – BasicEquation.ees
Now type in the nonlinear set of equations and solve for the 3 unknowns (use Ctrl+F to see the equations in formatted view)
The order in which the equations are entered does not matter at all!
Examples/Getting Started with EES/Solving multiple equations (BasicEqn.EES)
Use Ctrl+F to see the equations in formatted view (Windows > Formatted Equations).
0:00

## Slide 11: Formatting and Equations
Create a new EES worksheet and save it as
  EES Lecture 1.2 – EquationFormat.ees
Two types of comments:
  Comments in quotes are shown in formatted view
  Comments in curly brackets are not shown in formatted view
  "Equation Formatting" – this will be shown in formatted view
  "!Equation Formatting" – this will be shown in red
  {Equation Formatting} – this will not be shown
  Can also highlight any text (select and then right-click)
0:05

## Slide 12: Formatting and Equations
  Ordinary variables and equations
  "Define some variables. Actually, they are really constants as you cannot later assign other values to any of them!"
  a = 1
  b = 2
  c = 3
  e = 4
  "!A more complex equation using these variables"
  sqrt(1 + (a+b)/c + d) = e "Note the use of spaces!"
  Look at the formatted view!
  Note the position of the unknown “d” in the equation - it does not have to be on the left!
0:15

## Slide 13: Formatting and Equations
Arrays
  "This is how we define arrays"
  T[1] = 20
  T[4] = 25
  K[2,2] = 10 "This is a 2-D array (matrix)"
  Array indices are shown as subscripts. Note that arrays are also displayed in an array window (activate from the Windows menu and toolbar)
Raising the power
  "Raising power"
  k^2 = 5
  Exponents are shown as superscripts.
0:20

## Slide 14: Formatting and Equations
Absolute value
  "Absolute value"
  value_abs = abs(k)
  Look at the formatted view!
Clever Greek letters!
  "Clever Greek letters!"
  DELTAT = 1 or deltaP = 2
  OMEGA = 100 or omega = 100
  THETA = 45 or theta = 45
  Note: Although the formatted view distinguishes between upper and lower cases, the EES solver does not! Hence “OMEGA” and “omega” are regarded as the same variable!
0:22

## Slide 15: Formatting and Equations
General formatting
  "General formatting"
  y_old = 10 "Subscript"
  z|alpha = 9 "Superscript"
  x_dot = 10 "It understands dots & double dots!"
  x_ddot = 2 "Double dot"
  x_hat = 2 "Hat"
  x_bar = 22 "Over bar"
  angle|o = 20 "Superscript"
  T|star = 325 "Special superscript - star"
  Y|plus = 0.12 "Special superscript - plus"
  T_infinity = 25 "Often used to denote freestream"
  "Use the Ctrl+F to view!".
0:25

## Slide 16: Formatting and Equations
Compiler directives
  Start with a $
  Have a look at the Help system under the “Directives” heading
  Two directives that we will always use:
    $TabStops 0.5 cm
    $UnitSystem SI MASS C KPA KJ DEG
  Will also later look at the following directives:
    $If Condition
    ...
    $Else
    ...
    $EndIf
0:30

## Slide 17: Constants
EES defines a large number of constants. Check out Options > Constants. Of interest are the following:
  g# (gravity)
    So one can write
      F = m * g#
    Instead of
      g = 9.81 [m/s^2]
      F = m * g
  true#, false# (boolean tests)
  sigma# (Stefan-Boltzmann constant – radiation)
  C# (Speed of light)
  R# (Universal gas constant)
    So the Ideal Gas Constant for air would be:
    R_air = R# / MolarMass(Air)

## Slide 18
End of Lecture 1
0:05