## Slide 1: Computer Aided Engineering
Introduction to EES (Engineering Equation Solver) Lecture 3
Options menu
Parametric studies
& Plot basics

## Slide 2: Contents
EES introduction tutorial (4 Lectures)
  Solving nonlinear & implicit equations (Lect 1)
  Formatting of equations (Lect 1)
  The unit system (Lect 2)
  Built-in functions (Lect 2)
  The Options menu (Lect 3)
  Parametric studies & plot basics (Lect 3)
  Lookup tables (Lect 4)
  Plots (Lect 4)
0:35

## Slide 3: The Options Menu
Have a careful look at the functionality provided under the Options menu:
  Variable Info
  Function Info
  Unit Conversion Info
  Constants
  Unit System
  Stop Criteria
  Default Info
  Preferences.
0:25

## Slide 4: Parametric Study
A parametric study is in essence the study of the influence of variations in one or more variables (parameters) on the solution.
In most software, a parametric study is performed by repeatedly solving the model whilst making adjustments to the desired variables (parameters) in the form of a loop.
EES accomplishes this very elegantly by using a spreadsheet-like approach.
0:36

## Slide 5: Parametric Study Example
Let’s look at a really simple example
  (EES Lecture 3.1 - Simple ParametricTable.EES):
  Say you want to perform a calculation such as:
  But you want to perform this operation for several angles, say between 0 and 360 degrees.
  To do this in EES, simply enter this equation in the equations window
0:36
  But this solves y for only one angle!

## Slide 6: Parametric Study Example
A really simple example…:
  To calculate the value y for several angles, we could repeat the calculations using an array:
0:36
  But this is so tedious! And what if you want to have the y-values every 10 degrees instead of 45 degrees?

## Slide 7: Parametric Study Example
A really simple example…:
  So we define only the basic equation and tell EES to repeatedly solve the equation.
  Therefore, we cannot define theta with a fixed value as before:
  We now need to specify theta elsewhere in a repetitive way and solve the equation for each specified value of theta.
0:36

## Slide 8: Parametric Study Example
A really simple example…:
  EES does this in a particularly elegant way. It uses a spreadsheet to specify the variables that are to be specified as well at the variables for which the results are to be monitored:
  theta is now specified in the table, and EES will automatically list the results of y in the same table
0:36
Note each row is a new run!
Note the number of runs!

## Slide 9: Parametric Study Example
A really simple example…:
  The independent (specified) variables are simply typed into the EES parametric table. One can manually type in all the values, or utilise the quick-fill button:
0:36
Runs
Data specification
Filling
algorithm
Repeat
pattern

## Slide 10: Parametric Study Example
A really simple example…:
0:36
Run
Button
Independent
Variable (Black)
Dependent
Variable (Blue)
Note the units
Quick-fill
button
Table name

## Slide 11: Parametric Study
Demonstrate the following:
  Adding and deleting rows and variables to a parametric table
  Filling a parametric table column using:
    First & Last values
    First value and increment
    First value and multiplier
  Column and row popups and their functions
  Adding more parametric tables
  Deleting parametric tables.
So what is EES’s advantage over a spreadsheet (Excel)?
  Whilst Excel does an excellent job of repeated operations, complicated equations are difficult to manage and are never clear to a reader!
0:05

## Slide 12: Plot Basics
Engineering data is often best visualised by means of graphs (plots).
Plotting in EES is really easy. Once the data is available, a plot can be generated in the following simple steps:
  Select the plot type from the menu (e.g. X-Y)
  Select the data source (e.g. Parametric table or array)
  Select the dependent (Y-axis) and independent (X-axis) variables for plotting
  Select the plot formatting:
    Heading and description
    Line type and appearance (e.g spline, dot-dash, colour)
    Marker and legend, tics, grid lines, number format
    Automatic update from data source (on/off)
    Scale of axes, log or linear plot type etc
0:05

## Slide 13: Plot Basics
Create a new X-Y plot from the Plots menu as shown:
0:00
Note the data source!
Source can be:
Parametric Table
Lookup Table
Array
You can specify more than one Y-axis variable

## Slide 14: Plot Basics
The plot should look like this:
0:00
Each additional plot adds a new tab to the plot window.
You can of course have more than one graph on the same plot.
Legend
item
Spline fit
Marker
symbol
Plot title

## Slide 15: Parametric Study
Lets create a more realistic model on which we can do a parametric study
  (EES Lecture 3.2 - Projectile ParametricTable.EES):
  A simple projectile movement is used to demonstrate the use of a parametric study.
  We can modify the angle theta as well as the initial velocity u either individually or simultaneously and determine their influence on the maximum distance that the projectile will travel.
0:37

## Slide 16: Parametric Study
  "Equations of motion"
  v = u + a * t
  s = u * t + (1/2) * a * t^2
To calculate the maximum distance, calculate the time the projectile needs to reach maximum height by applying the first equation to the vertical velocity component (v = 0 and a = g). The total time will be twice this amount.
Now apply this total time to the horizontal velocity (which remains constant) using the second equation. The x-acceleration in the second equation is obviously zero."
0:40

## Slide 17: Parametric Study
So the equations will be as follows (remember the unit system!):
  $UnitSystem SI MASS C KPA KJ DEG
  $TabStops 0.5 cm
  "Equations of motion
  v = u + a * t Eq. 1
  s = u * t + (1/2) * a * t^2 Eq. 2"
  "Define initial values"
  u = 30 [m/s]
  theta = 45 [deg] "This must be commented if you run the parametric table“
  "Calculations"
  u_x = u * cos(theta) "X-component velocity"
  u_y = u * sin(theta) "Y-component velocity"
  t = 2 * u_y / g# "Time needed to max distance – from Eq. 1"
  s = u_x * t "Max distance – from Eq. 2"
  Note: We did not need to transpose Eq.1 and Eq.2 for EES to solve it!
0:45

## Slide 18: Parametric Study
Solve the model and observe the results:
0:48
But these results are only for theta = 45 deg and u = 30 m/s !

## Slide 19: Parametric Study
Now create a Parametric table by adding theta, s, t, ux and uy to it and vary theta from 0 to 90:
0:55
Remember to comment out {theta = 45 [deg]}
In the Equations Window!

## Slide 20: Parametric Study
Sometimes it is desirable to be able to run the basic worksheet without the parametric table (typically a basic test value case) and then to be able to run the parametric table, or even having and running different parametric tables.
It is then not a good idea to have to comment out the independent variables in the worksheet as shown before as it could become very confusing which variables have to be commented out and which variables have to be placed back in action.
Again, EES handles this very elegantly with a set of very simple directives
As shown before, directives start with a $, e.g.
  $IF ParametricTable
0:55

## Slide 21: Parametric Study
So, instead of commenting out the angle as we did before:
{theta = 45 [deg]}
We could do the following:
$IfNot ParametricTable
theta = 45 [deg]
$EndIf
Here, theta is defined as 45 deg when we are NOT running the parametric table, and effectively commented out when we DO!
0:55

## Slide 22: Parametric Study
Say for instance we have two parametric tables. In the first one (Table 1) we want to vary theta between 0 and 90 deg but keep u constant at 30 m/s. In the second table (Table 2) we want to keep theta constant at 45 deg and vary u between 10 and 50 m/s. The following code would automatically activate and deactivate the appropriate code:
  $If ParametricTable = 'Table 1'
  u = 30 [m/s]
  $EndIf
  $If ParametricTable = 'Table 2'
  theta = 45 [deg]
  $EndIf
  "This is for when we are NOT running any parametric tables (F2)"
  $IfNot ParametricTable
  u = 30 [m/s]
  theta = 45 [deg]
  $EndIf
0:55
Check out the online help for “Directives” under the “Special Topics” heading for the complete list of directives

## Slide 23: Parametric Study
Note that the active statements will appear in black whilst the inactive statements will appear in grey. In the following code, Table 1 was run:
  $If ParametricTable = 'Table 1'
  u = 30 [m/s]
  $EndIf
  $If ParametricTable = 'Table 2'
  theta = 45 [deg]
  $EndIf
  $IfNot ParametricTable
  u = 30 [m/s]
  theta = 45 [deg]
  $EndIf
0:55

## Slide 24: Create the Plot
Create a new X-Y plot from the Plots menu as shown:
0:00
Note the data source!
Source can be:
Parametric Table
Lookup Table
Array
You can specify more than one Y-axis variable

## Slide 25: Create the Plot
The plot should look like this:
0:00
Each additional plot adds a new tab to the plot window.
You can of course have more than one graph on the same plot.

## Slide 26
End of Lecture 3
0:05